Braking Distance Worksheet

Name: ____________________________	Date: _____________________

| Coefficient of Friction | Surfaces/Condition |
| --- | --- |
| 0.8 | Rubber on pavement, tires in perfect shape, dry road |
| 0.7 | Rubber on pavement, average tires, dry road |
| 0.5 | Rubber on pavement, worn tires, dry road |
| 0.3 | Rubber on pavement, average tires, wet road |
| 0.15 | Rubber on pavement, average tires, icy road |
| 0.6 | Steel on steel (railroad), average conditions |
| 0.05 | Waxed skies on snow, average conditions |
| 0.04 | Teflon on Teflon |

Braking Distance Formula: D=V2/2GF

D=braking distance

V=velocity in feet per second. Feet per second is miles per hour times 1.467

G=the acceleration of gravity in feet per second squared (32.17)

F=the selected coefficient of friction

Using a calculator, use all listed coefficient of frictions (on page 2) and solve for D with the three different velocities shown on the chart, entering the results on the chart.

| Velocity In Miles per Hour | Braking Distance in Feet |
| --- | --- |
| 20 |  |
| 40 |  |
| 60 |  |

| Coefficient of Friction = 0.8 |
| --- |
| 20 mph |  |
| 40 mph |  |
| 60 mph |  |

| Coefficient of Friction = 0.7 |
| --- |
| 20 mph |  |
| 40 mph |  |
| 60 mph |  |

| Coefficient of Friction = 0.5 |
| --- |
| 20 mph |  |
| 40 mph |  |
| 60 mph |  |

| Coefficient of Friction = 0.3 |
| --- |
| 20 mph |  |
| 40 mph |  |
| 60 mph |  |

| Coefficient of Friction = 0.15 |
| --- |
| 20 mph |  |
| 40 mph |  |
| 60 mph |  |

Answer Key

| Coefficient of Friction = 0.8 |
| --- |
| 20 mph | 17 feet |
| 40 mph | 67 feet |
| 60 mph | 152 feet |

| Coefficient of Friction = 0.7 |
| --- |
| 20 mph | 19 feet |
| 40 mph | 76 feet |
| 60 mph | 172 feet |

| Coefficient of Friction = 0.5 |
| --- |
| 20 mph | 27 feet |
| 40 mph | 107 feet |
| 60 mph | 241 feet |

| Coefficient of Friction = 0.3 |
| --- |
| 20 mph | 45 feet |
| 40 mph | 178 feet |
| 60 mph | 401 feet |

| Coefficient of Friction = 0.15 |
| --- |
| 20 mph | 89 feet |
| 40 mph | 357 feet |
| 60 mph | 803 feet |